## Slide 1: Packet Sniffing and Spoofing

## Slide 2: How Packets are Constructed

## Slide 3: Socket APIs
Sockets allow communication between two different processes on the same or different machines
Stream Sockets - Delivery in a networked environment is guaranteed
Datagram Sockets - Delivery in a networked environment is not guaranteed
Raw Sockets - Provides users access to the underlying communication protocols. A raw socket receives or sends the raw datagram not including link layer headers

## Slide 4: Socket Interface
Source: https://0xbharath.github.io/art-of-packet-crafting-with-scapy/networking/socket_interface/index.html

## Slide 5: Layer 4: Transport Layer

## Slide 6: Layer 3: Network Layer

## Slide 7: Layer 2: Data Link Layer (MAC Layer)

## Slide 8: Sending UDP Packet Using Python

## Slide 9: Remarks
A pair (host, port) is used for the AF_INET address family, where host is a string representing either a hostname in Internet domain notation like ‘www.ucmo.edu’ or an IPv4 address like ‘1.2.3.4’, and port is an integer
Send data to the socket. Return the number of bytes sent. sendto() sends out individual packet
  socket.sendto(bytes, address)
The data sent must be in the binary format. You can use either encode() to convert the message into bytes or directly use the binary string (b’hello world’)
Notes: Sendto() sends out individual packet

## Slide 10: Sending TCP Packet Using Python

## Slide 11: Remark
Connect to a remote socket at address. The client and server will complete the TCP three-way handshake to establish the connection
  socket.connect(address)
Send data to the socket. Returns the number of bytes sent. The send() method can only be used with a connected socket
  socket.send(bytes)
The number of bytes sent by the send() method may be less than the size of the data passed in. Unlike send(), sendall() continues to send data from bytes until either all data has been sent or an error occurs. None is returned on success

## Slide 12: Netcat (nc)
The Swiss army knife of TCP/IP connections
Netcat takes Standard Input and sends it across the network
Receives data from the network and puts it on Standard Output
Messages from Netcat itself goes to Standard Error which is displayed on the Standard Output
Netcat
Std In
Std Out
Send packets
Receive Packets
Std Err
The System
The Network

## Slide 13: Netcat Usage Continued
Clients initiate connections
  # nc -nv [targetIP] [remote_port(s)]
Listeners wait for connections
  # nc -lvp [local_port]
Netcat (client mode initiates a connection)
Netcat (listen mode waits for a connection)
Std In
Std In
Std Out
Std Out
The Network

## Slide 14: Packet Sending Tools
Using netcat
Bash: /dev/tcp or /dev/udp pseudo device
Others: telnet, ping, etc.

## Slide 15: How Packets Are Received

## Slide 16: How Packets Are Received
NIC (Network Interface Card) is a physical or logical link between a machine and a network
Each NIC has a MAC address
Every NIC on the network will hear all the frames on the wire
NIC checks the destination address for every packet, if the address matches the cards MAC address, it is further copied into a buffer in the kernel
Notes: After copying into the kernel buffer, the card interrupts the CPU informing it about the availability of a new packet

## Slide 17: Promiscuous Mode
The frames that are not destined to a given NIC are discarded
When operating in promiscuous mode, NIC passes every frame received from the network to the kernel
If a sniffer program is registered with the kernel, it will be able to see all the packets
In Wi-Fi, it is called Monitor Mode
Notes: It should be noted that elevated or root privileges are required to put a NIC card in promiscuous mode

## Slide 18: Receiving UDP Packet Using Python

## Slide 19: Remark
Bind the socket to address. If you pass an empty string for the hostname or IP address, the server will accept connections on all available IPv4 interfaces (equivalent to ‘0.0.0.0’)
  socket.bind(address)
Receive data from the socket. The return value is a pair (bytes, address) where bytes is a bytes object representing the data received and address is the address of the socket sending the data. recvfrom() receives individual packet. The bufsize argument of 1024 used above is the maximum amount of data to be received at once. It doesn’t mean that recvfrom() will return 1024 bytes
  socket.recvfrom(bufsize)
Notes: Recvfrom() receives individual packet

## Slide 20: Receiving TCP Packet Using Python

## Slide 21: Remark
Enable a server to accept connections. The backlog specifies the number of unaccepted connections that the system will allow before refusing new connections. In Linux, the maximum values can be found via /proc/sys/net/core/somaxconn
  socket.listen([backlog])
The accept() method blocks execution and waits for an incoming connection. The return value is a pair (conn, address) where conn is a new socket object usable to send and receive data on the connection, and address is the client address bound to the socket on the other end of the connection
  socket.accept()
Receive data from the socket. The return value is a bytes object representing the data received (no client address)
  socket.recv(bufsize)
Notes: If conn.recv() returns an empty bytes object, b'', that signals that the client closed the connection and the loop is terminated

## Slide 22: Blocking Calls
A socket function or method that temporarily suspends your application is a blocking call
accept(), connect(), send(), and recv() block, meaning they don’t return immediately
Blocking calls have to wait on system calls (I/O) to complete before they can return a value
The caller, are blocked until they’re done or a timeout or other error occurs

## Slide 23: Remark
Running the TCP sever several times with too small delay between executions, could lead to this error
This is because the previous execution has left the socket in a TIME_WAIT state, and can’t be immediately reused
There is a socket flag to set, in order to prevent this, socket.SO_REUSEADDR
The SO_REUSEADDR flag tells the kernel to reuse a local socket in TIME_WAIT state, without waiting for its natural timeout to expire

## Slide 24: Multi Threading TCP Server

## Slide 25: Packet Sniffing
Packet sniffing describes the process of capturing live data as they flow across a network
How to get a copy of a packet? – use raw socket

## Slide 26: Packet Sockets
Packet sockets are used to receive or send raw packets at the link layer
  packet_socket = socket(AF_PACKET, int socket_type, int protocol);
socket_type: SOCK_RAW for raw packets including the link-level header
When protocol is set to htons(ETH_P_ALL), then all protocols are received
All incoming packets of that protocol type will be passed to the packet socket before they are passed to the protocols stack implemented in the kernel

## Slide 27: Packet Flow With/Without Filters

## Slide 28: Pcap API
The Packet Capture library provides a high level interface to packet capture systems
Linux: libpcap
Windows: WinPcap
Adopted by many tools
  Wireshark, tcpdump, snort, nmap, Scapy, etc.

## Slide 29: Useful Packet Filters
Protocol primitive
  ether, ip, ip6, arp, tcp, udp, icmp
Type primitive
  host [host]: only give me packets to or from that host
  net [network]: give me packets for that given network
  port [port_number]: only packets for that port
  portrange [start – end]: only packets in that range of ports
Direction primitive
  src, dst
Use “and” or “or” to combine
Use “not” to negate

## Slide 30: Examples
Show all TCP port 443 packets going to or from host 192.168.1.81
  tcp and port 443 and host 192.168.1.81
Show all UDP packets from 192.168.1.81
  udp and src host 192.168.1.81
Show all packets to or from 192.168.1.0/24 subnet and not display ARP packets
  net 192.168.1.0/24 and not arp

## Slide 31: Packet Sniffing Tools
Tcpdump
  Command line
  Good choice for containers (in the lab setup)
Wireshark
  GUI
  Good choices for the environment supporting GUI (not containers)
Scapy
  Implement your own sniffing tools

## Slide 32: Tcpdump Examples
tcpdump -n -i eth0
  -n: do not resolve the IP address to host name
  -i: sniffing on this interface
tcpdump -n -i eth0 -vvv “tcp port 179”
  -vvv: asks the program to produce more verbose output.
tcpdump -i eth0 -w /tmp/packets.pcap
  saves the captured packets to a PCAP file
  use Wireshark to display them

## Slide 33: Wireshark and Containers
Find the correct interface

## Slide 34: Packet Sniffing Using Scapy (1)

## Slide 35: Scapy’s sniff Function
Scapy’s in-built sniff() function helps us capture all traffic. It sniffs packets and return a list of packets
sniff() has count, filter, iface, lfilter, prn, timeout options
Argument prn that allows you to pass a function that executes with each packet sniffed
Can capture packets with link layer and above
Scapy sniffer is not designed to be super fast so it can miss packets sometimes

## Slide 36: Packet Sniffing Using Scapy (2)

## Slide 37: A Sniffer Example

## Slide 38: Packet Spoofing
In normal packet construction
  Only some selected header fields can be set by users
  OS set the other fields
Packet spoofing
  Set arbitrary header fields
  Using tools
  Using Scapy

## Slide 39: Packet Spoofing
When some critical information in the packet is forged, we refer to it as packet spoofing
Many network attacks rely on packet spoofing
Let’s see how to send packets with spoofing

## Slide 40: Spoofing ICMP Packets
Notes: Explain the layer stacking in Scapy: ip/icmp

## Slide 41: Spoofing UDP Packets

## Slide 42: Sniffing and Then Spoofing
In many situations, we need to capture packets first, and then spoof a response based on the captured packets.
Procedure (using UDP as example)
  Use PCAP API to capture the packets of interests
  Make a copy from the captured packet
  Replace the UDP data field with a new message and swap the source and destination fields
  Send out the spoofed reply

## Slide 43: Sniff Request and Spoof Reply: Code

## Slide 44: Packet Spoofing: Scapy v.s C
Python + Scapy
  Pros: constructing packets is very simple
  Cons: much slower than C code
C Program (using raw socket)
  Pros: much faster
  Cons: constructing packets is complicated
Hybrid Approach
  Using Scapy to construct packets
  Using C to slightly modify packets and then send packets

## Slide 45: Summary
Packet sniffing
  Using raw socket
  Using PCAP APIs
Packet spoofing using raw socket
Sniffing and the spoofing